## Slide 1: Solving Large-Scale Electricity Market Pricing Problems in Polynomial Time
Mete Ahunbay, Martin Bichler, Teodora Dobos, Johannes Knörr
TUM School of Computation, Information and Technology
Chair of Decision Sciences & Systems
OR 2024
September 2024

## Slide 2: Pricing in non-convex markets
  Electricity markets are non-convex markets:
    non-convex preferences: minimum production levels, startup-costs, etc.
  Day-ahead markets: compute an allocation and prices for the next day
  Two challenges:
I. Identifying an optimal allocation is NP-hard.
Desirable properties
Can we efficiently find a near-optimal allocation and prices
that satisfy budget balance?
Scalability issues
II. Walrasian equilibria (market-clearing prices)
may not exist.
Yes, with the markup mechanism!

## Slide 3: Outline
Electricity market model
Welfare maximization & pricing problems
Markup mechanism
Evaluation
Conclusions

## Slide 4: Electricity market model
Transmission network
Periods (24 hours)
Goods: electricity at each node for every period

## Slide 5: Electricity market model
Transmission network
Periods (24 hours)
Set of sellers
  production constraints (min-uptime, no-load cost, etc.)
  supply bids cost function
Goods: electricity at each node for every period

## Slide 6: Electricity market model
Transmission network
Periods (24 hours)
Set of sellers
Set of buyers
  price-inelastic demand
  price-elastic demand bids valuation function
Goods: electricity at each node for every period

## Slide 7: Electricity market model
Transmission network
Periods (24 hours)
Set of sellers
Set of buyers
DCOPF power flow approximation (Molzahn & Hiskens, 2019)
  linear approximation
Goods: electricity at each node for every period

## Slide 8: Outline
Electricity market model
Welfare maximization & pricing problems
Markup mechanism
Evaluation
Conclusions

## Slide 9: Welfare maximization problem (WMP)
Let be an allocation with
  : buyers’ fulfilled demand
  : sellers’ production
  : sellers’ commitment
  : flows
WMP is defined as
where the welfare is
Node-balance constraints
Price-inelastic demand fulfillment
Production constraints, etc.

## Slide 10: Pricing problem
For a convex market, the Welfare Theorems (Arrow & Debreu 1954) hold.
A primal solution and a dual solution form a Walrasian equilibrium.
Such a pair satisfies certain desirable properties:
Efficiency
Supply-demand balance
Envy-freeness
Budget balance

## Slide 11: Walrasian equilibria in electricity markets?
With non-convexities present, a Walrasian equilibrium might not exist.
Clearing the market
Seller makes a loss at
Buyer 1 makes a loss at
Indivisible
1 Unit
$10
Indivisible
2 Units
$30
Seller
?
Indivisible
1 Unit
$28
Buyer 2
Buyer 1

## Slide 12: Individual rationality in electricity markets
No guarantee that prices satisfy individual rationality market participants make no loss
Make-whole payments (MWPs): compensations for the negative utility of a market participant , given prices and allocation :

## Slide 13: Individual rationality in electricity markets
No guarantee that prices satisfy individual rationality market participants make no loss
Make-whole payments (MWPs): compensations for the negative utility of a market participant , given prices and allocation :
Budget balance: market requires no external money to pay MWPs

## Slide 14: How to compute prices?
Integer Programming (IP) Pricing (O’Neill et al., 2005)
  standard approach used in the US
  “marginal pricing“ for non-convex markets
  good congestion signals, but large MWPs

## Slide 15: Outline
Electricity market model
Welfare maximization & pricing problems
Markup mechanism
Evaluation
Conclusions

## Slide 16: Markup mechanism
Observation: If no Walrasian equilibrium exists, any (price, allocation) pair must feature either:
  supply > demand budget deficit
  demand > supply rationing
Milgrom & Watt, 2022 proposed the markup mechanism for two-sided uncoupled markets – characteristics:
  near-optimal allocation
  buyers pay higher prices to cover the excess supply
  convex optimization

## Slide 17: Markup mechanism for electricity markets
Phase 1: Valuations scaling & convexifying WMP
Phase 2: Rounding & Residual Clearing
  Option 1: Rounding with a threshold
  Option 2: Rounding by solving a small MILP

## Slide 18: Markup mechanism for electricity markets
Phase 1: Valuations scaling & convexifying WMP
obtain
Phase 2: Rounding & Residual Clearing – Option 1: Rounding with a threshold

## Slide 19: Markup mechanism for electricity markets
Phase 1: Valuations scaling & convexifying WMP
obtain
Phase 2: Rounding & Residual Clearing – Option 2: Rounding by solving a small MILP
}

## Slide 20: What about the prices?
Prices are obtained from the dual problem of the convexified WMP.
Sellers‘ prices are and buyers’ prices are .
Role of : ensure that the market has no budget deficit:
No guarantee that such exists!

## Slide 21: Outline
Electricity market model
Welfare maximization & pricing problems
Markup mechanism
Evaluation
Conclusions

## Slide 22: Data sets
Scenario | Nodes | Lines | Sellers | Buyers | Demand (GWh) | Supply (GWh)
1. | 617 | 841 | 94 | 404 | 506 | 830
2. | 2,020 | 2,709 | 194 | 1,392 | 622 | 1,041
3. | 8,718 | 26,084 | 321 | 5,819 | 988 | 1,088
4. | 10,480 | 16,253 | 750 | 6,871 | 2,033 | 2,289
5. | 12,209 | 30,500 | 2,009 | 6,987 | 2,391 | 3,328
6. | 18,889 | 57,630 | 898 | 12,273 | 2,686 | 2,916
6 scenarios from the ARPA-E Challenge 2 extended to 24 hours

## Slide 23: Data sets
Scenario | Nodes | Lines | Sellers | Buyers | Demand (GWh) | Supply (GWh)
1. | 617 | 841 | 94 | 404 | 506 | 830
2. | 2,020 | 2,709 | 194 | 1,392 | 622 | 1,041
3. | 8,718 | 26,084 | 321 | 5,819 | 988 | 1,088
4. | 10,480 | 16,253 | 750 | 6,871 | 2,033 | 2,289
5. | 12,209 | 30,500 | 2,009 | 6,987 | 2,391 | 3,328
6. | 18,889 | 57,630 | 898 | 12,273 | 2,686 | 2,916
ISO-NE | 1,216 | - | 98 | 139 | 380 | 2,151
PJM | 13,431 | - | 1,217 | 366 | 2,204 | 4,907
6 scenarios from the ARPA-E Challenge 2 extended to 24 hours

## Slide 24: Experiments overview
Notes: Applied IP on OPT

## Slide 25: Result 1: Close approximation of OPT
Relative welfare loss

## Slide 26: Result 2: Fast method

## Slide 27: Result 3: No budget deficit
*A quantity in paratheses indicates budget surplus

## Slide 28: Outline
Electricity market model
Welfare maximization & pricing problems
Markup mechanism
Evaluation
Conclusions

## Slide 29: Conclusions
Electricity markets need to solve very large non-convex problems and determine prices.
Runtime limits are a concern.
The markup mechanism computes a near-optimal allocation in polynomial time.
The markup mechanism relies on two hyperparameters.
Buyers pay slightly higher prices to cover the make-whole payments.
The markup mechanism is a practical recommendation for large electricity markets.
Notes: Why it works well: >>cont var but <<int vars
Downsides: alpha, hyperparams to explore –> solve larger instances
MIP gap is small, same for alpha -> practical recommendation

## Slide 30: Thanks!
Our paper

## Slide 31: References
Milgrom P, Watt M (2022) Walrasian mechanisms for non-convex economies and the bound-form first welfare theorem. Proceedings of the ACM Conference of Economics and Computation
Neill, Hytowitz, Whitman, Mead, Dautel, Chen, Eldridge, Siskind, Kheloussi, Kolkmann, Smith, Castillo, Mays: Essays on average incremental cost pricing for independent system operators. 2019
Ahunbay, Bichler, Knoerr: Pricing optimal outcomes in coupled and non-convex markets: Theory and applications to electricity markets, Operations Research 2024, https://doi.org/10.1287/opre.2023.0401
Molzahn, D.K., Hiskens, I.A., 2019. A survey of relaxations and approximations of the power flow equations. Found. Trends® Electr. Energy Syst. 4 (1–2), 1–221. http://dx.doi.org/10.1561/3100000012.
Liberopoulos, Andrianesis: Critical review of pricing schemes in markets with non-convex costs. 2016. Operations Research 64(1):17–31
Starr RM, Quasi-equilibria in markets with non-convex preferences. Econometrica 37(1):25, ISSN 00129682, URL http://dx.doi.org/10.2307/1909201.
O’Neill RP, Sotkiewicz PM, Hobbs BF, Rothkopf MH, Stewart WR (2005) Efficient market-clearing prices in markets with nonconvexities. European Journal of Operational Research 1(164):269–285, URL https://doi.org/10.1016/j.ejor.2003.12.011